## Slide 1: DSP-CIS Part-IV : Filter Banks & Time-Frequency Transforms Chapter-11 : Filter Bank Preliminaries
Marc Moonen
Dept. E.E./ESAT-STADIUS, KU Leuven
marc.moonen@kuleuven.be
www.esat.kuleuven.be/stadius/

## Slide 2: Part-IV : Filter Banks & Time-Frequency Transforms
Filter Bank Preliminaries
        Filter Bank Set-Up
        Filter Bank Applications
        Ideal Filter Bank Operation
        Non-Ideal Filter Banks: Perfect Reconstruction Theory
      Filter Bank Design
        Filter Bank Design Problem Statement
        General Perfect Reconstruction Filter Bank Design
        Maximally Decimated DFT-Modulated Filter Banks
        Oversampled DFT-Modulated Filter Banks
    Frequency Domain Filtering
    Time-Frequency Analysis & Scaling
Chapter-11
Chapter-12
Chapter-13
Chapter-14

## Slide 3: Filter Bank Set-Up
What we have in mind is this… :
- Signals split into frequency channels/subbands
- Per-channel/subband processing
- Reconstruction : synthesis of processed signal
- Applications : see below (audio coding etc.)
- In practice, this is implemented as a multi-rate structure for higher
efficiency (see next slides)
subband processing
subband processing
subband processing
subband processing
H0(z)
H1(z)
H2(z)
H3(z)
IN
+
OUT
H0
H3
H2
H1
subband filters

## Slide 4: Filter Bank Set-Up
Step-1: Analysis filter bank
- Collection of N filters (`analysis filters’, `decimation filters’) with a
common input signal
- Ideal (but non-practical) frequency responses = ideal bandpass filters
- Typical frequency responses (overlapping, non-overlapping,…)
H0
H3
H2
H1
H0
H3
H2
H1
H0
H3
H2
H1
H0(z)
H1(z)
H2(z)
H3(z)
IN
N=4

## Slide 5: Filter Bank Set-Up
Step-2: Decimators (downsamplers)
- To increase efficiency, subband sampling rate is reduced by factor D
(= Nyquist sampling theorem (for passband signals) )
- Maximally decimated filter banks (=critically downsampled):
# subband samples = # fullband samples
this sounds like maximum efficiency, but aliasing (see below)!
- Oversampled filter banks (=non-critically downsampled):
# subband samples > # fullband samples
D=N
D<N
H0(z)
H1(z)
H2(z)
3
3
3
3
H3(z)
IN
N=4
D=3
PS: analysis filters Hn(z) are now also
decimation/anti-aliasing filters
to avoid aliasing in subband signals
after decimation (see Chapter-2)

## Slide 6: Filter Bank Set-Up
Step-3: Subband processing
- Example :
coding (=compression) + (transmission or storage) + decoding
- Filter bank design mostly assumes subband processing has `unit
transfer function’ (output signals=input signals), i.e. mostly ignores
presence of subband processing
subband processing
H0(z)
subband processing
H1(z)
subband processing
H2(z)
3
3
3
3
subband processing
H3(z)
IN
N=4
D=3

## Slide 7: Filter Bank Set-Up
Step-4&5: Expanders (upsamplers) & synthesis filter bank
- Restore original fullband sampling rate by D-fold upsampling
- Upsampling has to be followed by interpolation filtering (to ‘fill the
zeroes’ & remove spectral images, see Chapter-2)
- Collection of N filters (`synthesis’, `interpolation’) with summed output
- Frequency responses : preferably `matched’ to frequency responses
of the analysis filters (see below)
F0(z)
F1(z)
F2(z)
F3(z)
+
OUT
subband processing
3
H0(z)
subband processing
3
H1(z)
subband processing
3
H2(z)
3
3
3
3
subband processing
3
H3(z)
IN
N=4
D=3
F0
F3
F2
F1

## Slide 8: Filter Bank Set-Up
So this is the picture to keep in mind...
synthesis bank
(synthesis & interpolation)
upsampling/expansion
downsampling/decimation
analysis bank
(analysis & anti-aliasing)
F0(z)
F1(z)
F2(z)
F3(z)
+
OUT
subband processing
3
H0(z)
subband processing
3
H1(z)
subband processing
3
H2(z)
3
3
3
3
subband processing
3
H3(z)
IN
N=4
D=3

## Slide 9: Filter Bank Set-Up
A crucial concept concept will be Perfect Reconstruction (PR)
  Assume subband processing does not modify subband signals (e.g. lossless coding/decoding)
  The overall aim would then be to have PR, i.e. that the output signal is equal to the input signal up to at most a delay: y[k]=u[k-d]
  But: downsampling introduces aliasing, so achieving PR will be non-trivial
F0(z)
F1(z)
F2(z)
F3(z)
+
output = input
3
H0(z)
output = input
3
H1(z)
output = input
3
H2(z)
3
3
3
3
output = input
3
H3(z)
N=4
D=3
u[k]
y[k]=u[k-d]?

## Slide 10: Filter Bank Applications
Subband coding :
Coding = Fullband signal split into subbands & downsampled
(=analysis filters + decimators)
subband signals separately encoded
(e.g. subband with smaller energy content encoded with fewer bits)
Decoding = reconstruction of subband signals, then fullband
signal synthesis (=expanders + synthesis filters)
Example : Image coding (e.g. wavelet filter banks)
Example : Audio coding
e.g. digital compact cassette (DCC), MiniDisc, MPEG, ...
Filter bandwidths and bit allocations chosen to further
exploit perceptual properties of human hearing
(perceptual coding, masking, etc.)

## Slide 11: Filter Bank Applications
Subband adaptive filtering :
- Example : Acoustic echo cancellation
Adaptive filter models (time-varying) acoustic echo path and produces
a copy of the echo, which is then subtracted from microphone signal.
= Difficult problem !
✪ long acoustic impulse responses
✪ time-varying

## Slide 12: Filter Bank Applications
- Subband filtering = N (simpler) subband modeling problems instead
of one (more complicated) fullband modeling problem
- Perfect Reconstruction (PR) guarantees distortion-free desired
near-end speech signal
3
H0(z)
3
H1(z)
3
H2(z)
3
H3(z)
3
H0(z)
3
H1(z)
3
H2(z)
3
H3(z)
+
+
+
+
3
F0(z)
3
F1(z)
3
F2(z)
3
F3(z)
OUT
+
ad.filter
ad.filter
ad.filter
ad.filter
N=4
D=3

## Slide 13: Ideal Filter Bank Operation
With ideal analysis/synthesis filters, filter bank operates as follows (1)
subband processing
4
H0(z)
subband processing
4
H1(z)
subband processing
4
H2(z)
4
4
4
4
subband processing
4
H3(z)
IN
F0(z)
F1(z)
F2(z)
F3(z)
+
OUT
H0(z)
H1(z)
H2(z)
H3(z)
IN
…
…
analysis filters
input signal spectrum
(*) Similar figures for other D=N & for oversampled (D<N) case

## Slide 14: Ideal Filter Bank Operation
With ideal analysis/synthesis filters, filter bank operates as follows (2)
subband processing
4
H0(z)
subband processing
4
H1(z)
subband processing
4
H2(z)
4
4
4
4
subband processing
4
H3(z)
IN
F0(z)
F1(z)
F2(z)
F3(z)
+
OUT
H0(z)
H1(z)
H2(z)
H3(z)
x1
x1
…
…
PS: H0(z) analysis filter
≈ lowpass anti-aliasing filter

## Slide 15: Ideal Filter Bank Operation
With ideal analysis/synthesis filters, filter bank operates as follows (3)
subband processing
4
H0(z)
subband processing
4
H1(z)
subband processing
4
H2(z)
4
4
4
4
subband processing
4
H3(z)
IN
F0(z)
F1(z)
F2(z)
F3(z)
+
OUT
x’1
x’1
(ideal subband processing)
x’1
…
…

## Slide 16: Ideal Filter Bank Operation
With ideal analysis/synthesis filters, filter bank operates as follows (4)
subband processing
4
H0(z)
subband processing
4
H1(z)
subband processing
4
H2(z)
4
4
4
4
subband processing
4
H3(z)
IN
F0(z)
F1(z)
F2(z)
F3(z)
+
OUT
x”1
x”1
…
…

## Slide 17: Ideal Filter Bank Operation
With ideal analysis/synthesis filters, filter bank operates as follows (5)
subband processing
4
H0(z)
subband processing
4
H1(z)
subband processing
4
H2(z)
4
4
4
4
subband processing
4
H3(z)
IN
F0(z)
F1(z)
F2(z)
F3(z)
+
OUT
F0(z)
F1(z)
F2(z)
F3(z)
x’’’1
x’’’1
…
…
PS: F0(z) synthesis filter
≈ lowpass interpolation filter

## Slide 18: Ideal Filter Bank Operation
With ideal analysis/synthesis filters, FB operates as follows (6)
subband processing
4
H0(z)
subband processing
4
H1(z)
subband processing
4
H2(z)
4
4
4
4
subband processing
4
H3(z)
IN
F0(z)
F1(z)
F2(z)
F3(z)
+
OUT
x2
…
…
H0(z)
H1(z)
H2(z)
H3(z)
x2
PS: H1(z) analysis filter
≈ bandpass anti-aliasing filter

## Slide 19: Ideal Filter Bank Operation
With ideal analysis/synthesis filters, filter bank operates as follows (7)
subband processing
4
H0(z)
subband processing
4
H1(z)
subband processing
4
H2(z)
4
4
4
4
subband processing
4
H3(z)
IN
F0(z)
F1(z)
F2(z)
F3(z)
+
OUT
x’2
x’2
…
x’2

## Slide 20: Ideal Filter Bank Operation
With ideal analysis/synthesis filters, filter bank operates as follows (8)
subband processing
4
H0(z)
subband processing
4
H1(z)
subband processing
4
H2(z)
4
4
4
4
subband processing
4
H3(z)
IN
F0(z)
F1(z)
F2(z)
F3(z)
+
OUT
x”2
IN
…
…
x”2

## Slide 21: Ideal Filter Bank Operation
With ideal analysis/synthesis filters, filter bank operates as follows (9)
subband processing
4
H0(z)
subband processing
4
H1(z)
subband processing
4
H2(z)
4
4
4
4
subband processing
4
H3(z)
IN
F0(z)
F1(z)
F2(z)
F3(z)
+
OUT
…
…
PS: F1(z) synthesis filter
≈ bandpass interpolation filter
F0(z)
F1(z)
F2(z)
F3(z)
x”’2
x”’2

## Slide 22: Ideal Filter Bank Operation
With ideal analysis/synthesis filters, filter bank operates as follows (10)
subband processing
4
H0(z)
subband processing
4
H1(z)
subband processing
4
H2(z)
4
4
4
4
subband processing
4
H3(z)
IN
F0(z)
F1(z)
F2(z)
F3(z)
+
OUT
Now try this with non-ideal filters…?
…
…
OUT=IN
=Perfect Reconstruction

## Slide 23: Non-Ideal Filter Bank Operation
Question :
Can y[k]=u[k-d] be achieved with non-ideal filters
i.e. in the presence of aliasing ?
Answer :
YES !! Perfect Reconstruction Filter Banks (PR-FB)
with synthesis bank designed to remove aliasing effects !
F0(z)
F1(z)
F2(z)
F3(z)
+
output = input
3
H0(z)
output = input
3
H1(z)
output = input
3
H2(z)
3
3
3
3
output = input
3
H3(z)
N=4
D=3
u[k]
y[k]=u[k-d]?

## Slide 24: Non-Ideal Filter Bank Operation
A very simple PR-FB is constructed as follows
- Starting point is this…
As y[k]=u[k-d] this can be viewed as a (1st) (maximally decimated) PR-FB
(with lots of aliasing in the subbands!)
All analysis/synthesis filters are seen to be pure delays,
hence are not frequency selective (i.e. far from ideal
case with ideal bandpass filters, not yet very interesting….)
4
4
4
4
+
u[k-3]
4
4
4
4
u[k]
0,0,0,u[0],0,0,0,u[4],0,0,0,...
0,0,u[-1],0,0,0,u[3],0,0,0,0,...
0,u[-2],0,0,0,u[2],0,0,0,0,0,...
u[-3],0,0,0,u[1],0,0,0,0,0,0,...
(*) Similar figures for other D=N

## Slide 25: Non-Ideal Filter Bank Operation
- Now insert DFT-matrix (discrete Fourier transform)
and its inverse (I-DFT)...
as this clearly does not change the input-output relation (hence PR property preserved)
4
4
4
4
+
u[k-3]
4
4
4
4
u[k]



## Slide 26: Non-Ideal Filter Bank Operation
- …and reverse order of decimators/expanders and DFT-matrices (not done in an efficient implementation!) :
=analysis filter bank =synthesis filter bank
This is the `DFT/IDFT filter bank’
It is a first (or 2nd) example of a (maximally decimated) PR-FB!
4
4
4
4
4
4
4
4
+
u[k-3]
u[k]

## Slide 27: Non-Ideal Filter Bank Operation
What do analysis filters look like? (N-channel case)
This is seen/known to represent a collection of filters Ho(z),H1(z),...,
each of which is a frequency shifted version of Ho(z) :
i.e. the Hn are obtained by uniformly shifting the `prototype’ Ho over the
frequency axis.
u[k]
N=4

## Slide 28: Non-Ideal Filter Bank Operation
The prototype filter Ho(z) is a not-so-great
lowpass filter with significant sidelobes.
Ho(z) and Hi(z)’s are thus far from ideal
lowpass/bandpass filters.
Synthesis filters are shown to be equal to analysis filters (up to a scaling)
Hence (maximal) decimation introduces
significant ALIASING in the decimated
subband signals
Still, we know this is a PR-FB (see construction previous slides), which means the synthesis filters can apparently restore the aliasing distortion.
This is remarkable, it means PR can be achieved even with non-ideal filters!
Ho(z)
H3(z)
N=4
H1(z)
H2(z)

## Slide 29: Perfect Reconstruction Theory
Now comes the hard part…(?)
2-channel case:
Simple (maximally decimated, D=N) example to start with…
✪ N-channel case:
Polyphase decomposition based approach

## Slide 30: Perfect Reconstruction : 2-Channel Case
It is proved that... (try it!)
U(-z) represents aliased signals (*), hence A(z) is referred to as `alias transfer function’
T(z) referred to as `distortion function’ (amplitude & phase distortion) Note that T(z) is also the transfer function obtained after removing the up- and downsampling (up to a scaling) (!)
H0(z)
H1(z)
2
2
u[k]
2
2
F0(z)
F1(z)
+
y[k]

## Slide 31: Perfect Reconstruction : 2-Channel Case
Requirement for `alias-free’ filter bank :
If A(z)=0, then Y(z)=T(z).U(z)
hence the complete filter bank behaves as a LTI system
(despite/without up- & downsampling)!
Requirement for `perfect reconstruction’ filter bank
(= alias-free + distortion-free):
H0(z)
H1(z)
2
2
u[k]
2
2
F0(z)
F1(z)
+
y[k]

## Slide 32: Perfect Reconstruction : 2-Channel Case
A solution is as follows: (ignore details) [Smith&Barnwell 1984] [Mintzer 1985]
i)
so that (alias cancellation)
ii) `power symmetric’ Ho(z) (real coefficients case)
iii)
so that (distortion function) ignore the details!
This is a so-called`paraunitary’ perfect reconstruction bank (see below),
based on a lossless system Ho,H1 :
This is already pretty complicated…



## Slide 33: Perfect Reconstruction : N-Channel Case
It is proved that... (try it!)
2nd term represents aliased signals, hence all `alias transfer functions’ An(z) should ideally be zero (for all n=1..N-1)
T(z) is referred to as `distortion function’ (amplitude & phase distortion). For perfect reconstruction, T(z) should be a pure delay
H2(z)
H3(z)
4
4
4
4
F2(z)
F3(z)
y[k]
H0(z)
H1(z)
4
4
u[k]
4
4
F0(z)
F1(z)
+
Sigh !!…Too Complicated!!...
D=N=4

## Slide 34: Perfect Reconstruction Theory
A simpler analysis results from a polyphase description :
n-th row of E(z) has N-fold (=D-fold)
polyphase components of Hn(z)
n-th column of R(z) has N-fold
polyphase components of Fn(z)
4
4
4
4
+
u[k-3]
u[k]
4
4
4
4
Do not continue until you understand how formulae correspond to block scheme!
D=N=4

## Slide 35: Perfect Reconstruction Theory
With the `noble identities’, this is equivalent to:
Necessary & sufficient conditions for
i) alias cancellation
ii) perfect reconstruction
are then derived, based on the product
4
4
4
4
+
u[k-3]
u[k]
4
4
4
4
D=N=4

## Slide 36: Perfect Reconstruction Theory
i) Necessary & sufficient condition for alias-free FB is…:
a pseudo-circulant matrix is a circulant matrix with the additional feature
that elements below the main diagonal are multiplied by 1/z, i.e.
& then 1st row of R(z).E(z) are polyphase cmpnts of `distortion function’ T(z)
4
4
4
4
+
u[k-3]
u[k]
4
4
4
4
Read on 
D=N=4
D=N=4

## Slide 37: Perfect Reconstruction Theory
This can be verified as follows:
First, previous block scheme is equivalent to (cfr. Noble identities)
Then (iff R.E is pseudo-circ.)…
So that finally..
4
4
4
4
+
u[k]
4
4
4
4
4
4
4
4
4
+
T(z)*u[k-3]
4
4
4
u[k]
Read on 
D=N=4
D=N=4

## Slide 38: Perfect Reconstruction Theory
ii) Necessary & sufficient condition for PR is then…
(i.e. where T(z)=pure delay, hence pr(z)=pure delay=z-δ, and all other pn(z)=0)
In is nxn identity matrix, r is arbitrary
Example (r=0) : for conciseness, will
use this from now on !
 PR-FB design in chapter-12
4
4
4
4
+
u[k-3]
u[k]
4
4
4
4
Beautifully simple!! (compared to page 33)
D=N=4

## Slide 39: Perfect Reconstruction Theory
A similar PR condition can be derived for oversampled FBs
The polyphase description (compare to p.34) is then…
n-th row of E(z) has D-fold
polyphase components of Hn(z)
n-th column of R(z) has D-fold
polyphase components of Fn(z)
Note that E is an N-by-D (‘tall-thin’) matrix, R is a D-by-N (‘short-fat’) matrix !
u[k]
4
4
4
4
4
4
4
4
+
u[k-3]
4
4
4
4
D=4 N=6

## Slide 40: Perfect Reconstruction Theory
Simplified (r=0 on p.38) condition for PR is then…
In the D=N case (p.38), the PR condition has a product of square matrices. PR-FB design (Chapter 11) will then involve matrix inversion, which is mostly problematic.
In the D<N case, the PR condition has a product of a ‘short-fat’ matrix and a ‘tall-thin’ matrix. This will lead to additional PR-FB design flexibility (see Chapter 12).
Again beautifully simple!! (compared to page 33)
DxD
DxN
NxD
u[k]
4
4
4
4
4
4
4
4
+
u[k-3]
4
4
4
4
D=4 N=6