## Slide 1: DSP-CIS Part-II: Filter Design and Implementation Chapter-4 : Filter Design
Marc Moonen
Dept. E.E./ESAT-STADIUS, KU Leuven
marc.moonen@kuleuven.be
www.esat.kuleuven.be/stadius/

## Slide 2: Filter Design Process
Step-1 : Define filter specs
Pass-band, stop-band, optimization criterion,…
Step-2 : Derive optimal transfer function
FIR or IIR filter design
Step-3 : Filter realization (block scheme/flow graph)
Direct form realizations, lattice realizations,…
Step-4 : Filter implementation (software/hardware)
Finite word-length issues, …
Question: implemented filter = designed filter ?
‘You can’t always get what you want’ -Jagger/Richards (?)
Chapter-4
Chapter-5
Chapter-6

## Slide 3: Filter Design Process
Step-1: Filter Specification
Example: Low-pass filter

## Slide 4: Chapter-4 : Filter Design
FIR filters
  Linear-phase FIR filters
  FIR design by optimization
  Weighted least-squares design, Minimax design
  FIR design in practice
  `Windows’, Equiripple design, …
  Software (Matlab,…)
IIR filters
  Poles and zeros
  IIR design by optimization
  Weighted least-squares design, Minimax design
  IIR design in practice
  Software (Matlab,…)

## Slide 5: FIR Filters
FIR filter = finite impulse response filter
L poles at the origin z=0 (hence guaranteed stability)
L zeros (zeros of B(z)), `all zero’ filters
Corresponds to difference equation
Hence also known as `moving average filters’ (MA)
Impulse response

## Slide 6: Linear Phase FIR Filters
Non-causal zero-phase filters :
Example: symmetric impulse response (length 2.Lo+1)
h[-Lo],….h[-1], h[0] ,h[1],...,h[Lo]
h[k]=h[-k], k=1..Lo
Frequency response is
i.e. real-valued (=zero-phase) transfer function
k
Lo
2Lo+1 terms
Lo+1 terms

## Slide 7: Linear Phase FIR Filters
Causal linear-phase filters = non-causal zero-phase + delay
Example: symmetric impulse response & L even
h[0],h[1],….,h[L]
L=2.Lo
h[k]=h[L-k], k=0..L
Frequency response is
= i.e. causal implementation of zero-phase filter, by
introducing delay
k
L
0
 phase is linear function
of frequency

## Slide 8: Linear Phase FIR Filters
Type-1 Type-2 Type-3 Type-4
L=2Lo=even L=2Lo+1=odd L=2Lo=even L=2Lo+1=odd
symmetric symmetric anti-symmetric anti-symmetric
h[k]=h[L-k] h[k]=h[L-k] h[k]=-h[L-k] h[k]=-h[L-k]
zero at zero at zero at
LP/HP/BP LP/BP BP HP/BP
PS: `Modulating’ Type-2 with 1,-1,1,-1,.. gives Type-4 (LP->HP)
PS: `Modulating’ Type-4 with 1,-1,1,-1,.. gives Type-2 (HP->LP)
PS: `Modulating’ Type-1 with 1,-1,1,-1,.. gives Type-1 (LP<->HP)
PS: `Modulating’ Type-3 with 1,-1,1,-1,.. gives Type-3 (BP<->BP)
PS: IIR filters can NEVER have linear-phase property ! (proof see literature)

## Slide 9: FIR Filter Design by Optimization
Weighted Least Squares Design :
Select one of the basic forms that yield linear phase
e.g. Type-1
Specify desired frequency response (LP,HP,BP,…)
Optimization criterion is
where is a weighting function

## Slide 10: FIR Filter Design by Optimization
This is `Quadratic Optimization’ problem
… with solution

## Slide 11: FIR Filter Design by Optimization
Example: Low-pass design
Optimization function is
i.e.

## Slide 12: FIR Filter Design by Optimization
A simpler problem is obtained by replacing the F(..) by…
where the wi’s are a set of sample frequencies
This leads to an equivalent (`discretized’) quadratic optimization function:
+++ Simple
- - - Unpredictable behavior in between sample freqs.
Compare to p.10

## Slide 13: FIR Filter Design by Optimization
This is often supplemented with additional constraints, e.g. for pass-band and stop-band ripple control :
The resulting optimization problem is :
minimize : (=quadratic function)
subject to (=pass-band constraints)
(=stop-band constraints)
= `Quadratic Programming’ problem

## Slide 14: FIR Filter Design by Optimization
`Minimax’ Design :
Select one of the basic forms that yield linear phase
e.g. Type-1
Specify desired frequency response (LP,HP,BP,…)
Optimization criterion is
where is a weighting function
Leads to `Semi-Definite Programming’ (SDP) problem, for which efficient interior-point algorithms & software are available.

## Slide 15: FIR Filter Design by Optimization
Conclusion:
(I) Weighted least squares design
(II) Minimax design
provide general `framework’, procedures to translate filter design problems into standard optimization problems
In practice (and in textbooks):
Emphasis on specific (ad-hoc) procedures :
- Filter design based on `windows’
- Equiripple design

## Slide 16: FIR Filter Design using `Windows’
Example : Low-pass filter design
Ideal low-pass filter is
Hence ideal time-domain impulse response is (non-causal zero-phase)
Truncate hd[k] to L+1 samples (L even):
Add delay to turn into causal filter

## Slide 17: FIR Filter Design using `Windows’
Example : Low-pass filter design (continued)
PS : It can be shown (use Parceval’s theorem) that the filter obtained by such time-domain truncation is also obtained by using a weighted least-squares design procedure with the given Hd (+linear phase) and weighting function
Truncation corresponds to applying a `rectangular window’ :
+++ Simple procedure (also for HP,BP,…)
- - - Truncation in time-domain results in `Gibbs effect’ in frequency domain, i.e. large ripple in pass-band and stop-band (at band edge discontinuity), which cannot be reduced by increasing the filter order L.

## Slide 18: FIR Filter Design using `Windows’
Remedy: Apply other window functions…
Time-domain multiplication with a window function w[k] corresponds to frequency domain convolution with W(z) :
Candidate windows : Han, Hamming, Blackman, Kaiser,…. (see textbooks, see DSP-I)
Window choice/design = trade-off between side-lobe levels (define peak pass-/stop-band ripple) and width main-lobe (defines transition bandwidth), see examples p.25-28

## Slide 19: FIR Equiripple Design
Starting point is minimax criterion, e.g.
Based on theory of Chebyshev approximation and the `alternation theorem’, which (roughly) states that the optimal d’s are such that the `max’ (maximum weighted approximation error) is obtained at Lo+2 extremal frequencies…
…that hence will exhibit the same maximum ripple (`equiripple’)
Iterative procedure for computing extremal frequencies, etc. (Remez exchange algorithm, Parks-McClellan algorithm)
Very flexible, etc., available in many software packages
Details omitted here (see textbooks)

## Slide 20: FIR Filter Design Software
FIR Filter design abundantly available in commercial software
Matlab:
b=fir1(L,Wn,type,window), windowed linear-phase FIR design, L is filter order, Wn defines band-edges, type is `high’,`stop’,…
b=fir2(L,f,m,window), windowed FIR design based on inverse Fourier transform with frequency points f and corresponding magnitude response m
b=remez(L,f,m), equiripple linear-phase FIR design with Parks-McClellan (Remez exchange) algorithm

## Slide 21: FIR Filter Design – Matlab Examples
1/8
for filter_order=10:30:100
% Impulse response
b = fir1(filter_order,[W1 W2],'bandpass');
% Frequency response
% Plotting
end
filter_order-10

## Slide 22: FIR Filter Design – Matlab Examples
2/8
for filter_order=10:30:100
% Impulse response
b = fir1(filter_order,[W1 W2],'bandpass');
% Frequency response
% Plotting
end
filter_order-40

## Slide 23: FIR Filter Design – Matlab Examples
3/8
for filter_order=10:30:100
% Impulse response
b = fir1(filter_order,[W1 W2],'bandpass');
% Frequency response
% Plotting
end
filter_order-70

## Slide 24: FIR Filter Design – Matlab Examples
4/8
for filter_order=10:30:100
% Impulse response
b = fir1(filter_order,[W1 W2],'bandpass');
% Frequency response
% Plotting
end
filter_order-100
% See help fir1
% Bandpass filter
% B = FIR1(N,Wn,'bandpass')
% Wn = [W1 W2] upper and lower cut-off freq
W1 = 0.25; % 1/4*pi
W2 = 0.75; % 3/4*pi
for filter_order=10:30:100
% Impulse response
b = fir1(filter_order,[W1 W2],'bandpass');
% Frequency response
[H W]=freqz(b);
% Plotting
subplot(211)
plot(W,db(abs(H)));hold on
set(gca,'XTick',0:pi/2:pi)
set(gca,'XTickLabel',{'0','pi/2','pi'})
title('FIR filter design');
xlabel('Circular frequency (Radians)');
ylabel('Magnitude response (dB)');
axis([0 pi -100 20])
subplot(212)
plot(b)
xlabel('Samples');
ylabel('Impulse response');
axis([0 100 -0.5 0.5])
pause
end
hold off

## Slide 25: FIR Filter Design – Matlab Examples
5/8

## Slide 26: FIR Filter Design – Matlab Examples
6/8

## Slide 27: FIR Filter Design – Matlab Examples
7/8

## Slide 28: FIR Filter Design – Matlab Examples
% See help fir1
% Bandpass filter
% B = FIR1(N,Wn,'bandpass',win)
% Wn = [W1 W2] upper and lower cut-off frequencies
% win windown type
W1 = 0.25; % 1/4*pi
W2 = 0.75; % 3/4*pi
filter_order = 50;
win1 = triang(filter_order+1);
win2 = rectwin(filter_order+1);
win3 = hamming(filter_order+1);
win4 = blackman(filter_order+1);
b1 = fir1(filter_order,[W1 W2],'bandpass',win1);
b2 = fir1(filter_order,[W1 W2],'bandpass',win2);
b3 = fir1(filter_order,[W1 W2],'bandpass',win3);
b4 = fir1(filter_order,[W1 W2],'bandpass',win4);
[H1 W] = freqz(b1);
[H2 W] = freqz(b2);
[H3 W] = freqz(b3);
[H4 W] = freqz(b4);
subplot(211)
plot(W,db(abs(H1)));hold on;plot(W,db(abs(H2)));plot(W,db(abs(H3)));plot(W,db(abs(H4)));hold off
set(gca,'XTick',0:pi/2:pi)
set(gca,'XTickLabel',{'0','pi/2','pi'})
title('Blackman window');
xlabel('Circular frequency (Radians)');
ylabel('Magnitude response (dB)');
axis([0 pi -100 20])
subplot(212)
plot(b4);hold on;plot(win4,'r');;hold off
xlabel('Samples');
ylabel('Impulse response');
axis([0 filter_order+1 -0.5 1.5])
8/8

## Slide 29: IIR filters
Rational transfer function :
L poles (zeros of A(z)) , L zeros (zeros of B(z))
Infinitely long impulse response
Stable iff poles lie inside the unit circle
Corresponds to difference equation
= also known as `ARMA’ (autoregressive-moving average)

## Slide 30: IIR Filter Design
+
Low-order filters can produce sharp frequency response
Low computational cost (cfr. difference equation p.29)
-
Design more difficult
Stability should be checked/guaranteed
Phase response not easily controlled
(e.g. no linear-phase IIR filters)
Coefficient sensitivity, quantization noise, etc. can be a problem (see Chapter-6)

## Slide 31: IIR filters
Frequency response versus pole-zero location :
( ~ Frequency response is z-transform
evaluated on the unit circle)
Example
Low-pass filter with
poles at
zeros at
Zero near (or on) unit-circle introduces `dip’ (or transmision zero) in freq. response
hence stop-band can be emphasized by zero placement
zero
pole
pole
DC (z=1)
Nyquist freq (z=-1)
Pole near unit-circle introduces `peak’ in frequency response
hence pass-band can be set by pole placement

## Slide 32: IIR Filter Design by Optimization
(I) Weighted Least Squares Design :
IIR filter transfer function is
Specify desired frequency response (LP,HP,BP,…)
Optimization criterion is
where is a weighting function
Stability constraint :

## Slide 33: IIR Filter Design by Optimization
(II) `Minimax’ Design :
IIR filter transfer function is
Specify desired frequency response (LP,HP,BP,…)
Optimization criterion is
where is a weighting function
Stability constraint :

## Slide 34: IIR Filter Design by Optimization
These optimization problems are significantly more
difficult than those for the FIR design case… :
Problem-1: Presence of denominator polynomial leads to non-linear/non-quadratic optimization
Problem-2: Stability constraint
(zeros of a high-order polynomial are related to the its
coefficients in a highly non-linear manner)
  Solutions based on alternative stability constraints, that e.g. are affine functions of the filter coefficients, etc…
  Topic of ongoing research, details omitted here

## Slide 35: IIR Filter Design by Optimization
Conclusion:
(I) Weighted least squares design
(II) Minimax design
provide general `framework’, procedures to translate filter design problems into ``standard’’ optimization problems
In practice (and in textbooks):
Emphasis on specific (ad-hoc) procedures :
- IIR filter design based analog filter design (Butterworth,
Chebyshev, elliptic,…) and analog->digital conversion
- IIR filter design by modeling = direct z-domain design
(Pade approximation, Prony, etc., not addressed here)

## Slide 36: IIR Filter Design Software
IIR filter design considerably more complicated than FIR design (stability, phase response, etc..)
(Fortunately) IIR Filter design abundantly available in commercial software
Matlab:
[b,a]=butter/cheby1/cheby2/ellip(L,…,Wn),
IIR LP/HP/BP/BS design based on analog prototypes, pre-warping,
bilinear transform, …
immediately gives H(z) 
analog prototypes, transforms, … can also be called individually
filter order estimation tool
etc...

## Slide 37: IIR Filter Design – Matlab Examples
Butterworth 2nd order
1/4

## Slide 38: IIR Filter Design – Matlab Examples
Butterworth 2nd , 10th order
2/4

## Slide 39: IIR Filter Design – Matlab Examples
Butterworth 2nd, 10th, 18th order
3/4

## Slide 40: IIR Filter Design – Matlab Examples
% See help butter
% Bandpass filter
% [B,A] = butter(filter_order,[W1 W2],'bandpass');
% Wn = [W1 W2] upper and lower cut-off frequencies
W1 = 0.25; % 1/4*pi
W2 = 0.75; % 3/4*pi
for filter_order=2:8:28
% Coefficients response
[B,A] = butter(filter_order,[W1 W2],'bandpass');
% Frequency response
[H W] = freqz(B,A);
% Impulse response
h = filter(B,A,[zeros(2,1);1;zeros(100,1)]);
% Plotting
subplot(211)
plot(W,db(abs(H)));hold on
set(gca,'XTick',0:pi/2:pi)
set(gca,'XTickLabel',{'0','pi/2','pi'})
title('IIR filter design');
xlabel('Circular frequency (Radians)');
ylabel('Magnitude response (dB)');
axis([0 pi -100 20])
subplot(212)
plot(h)
xlabel('Samples');
ylabel('Impulse response');
axis([0 100 -0.5 0.5])
pause
end
hold off
Butterworth 2nd, 10th, 18th, 26th order
4/4