## Slide 1: Digital Audio Signal Processing DASP Chapter-2 Single-Channel Noise Reduction
Marc Moonen & Arnout Roebben
Dept. E.E./ESAT-STADIUS, KU Leuven
marc.moonen@kuleuven.be
homes.esat.kuleuven.be/~moonen/

## Slide 2: Single-Channel Noise Reduction
Microphone signal is
Goal: Estimate s[k] based on y[k]
Applications:
  Speech enhancement in conferencing, handsfree telephony, hearing aids, …
  Automatic speech recognition
  Digital audio restoration
desired signal
estimate
desired signal s[k]
noise signal(s)
?
y[k]
desired signal
contribution
noise
contribution

## Slide 3: Single-Channel Noise Reduction
Will consider methods that do not rely on a priori information (e.g. expected noise spectrum)
Will consider speech applications: s[k] = speech signal
  Speech is on/off signal, where speech pauzes can be used to estimate noise spectrum
desired signal
estimate
desired signal s[k]
noise signal(s)
?
y[k]
desired signal
contribution
noise
contribution

## Slide 4: Overview
Frequency Domain Methods /
Spectral Subtraction Methods
  Spectral subtraction basics
  Gain functions
  Realization
  Musical noise
  Signal model based spectral subtraction
Time Domain Methods
  Kalman Filter Based Noise Reduction
  Subspace Methods

## Slide 5: Spectral Subtraction: Basics
Signal segmented into `frames’ (e.g. 10..20msec), for each frame a frequency domain representation (=spectrum) is
(i-th frame)
However, as speech signal is an on/off signal, some frames have speech+noise, i.e.
some frames have noise only, i.e.
A speech detection algorithm (a.k.a. ‘voice activity detection’, VAD) is needed to distinguish between these 2 types of frames (based on energy/dynamic range/statistical properties,…)

## Slide 6: Spectral Subtraction: Basics
Definition:
i.e. noise spectrum expected magnitude & power (frame i)
Assumption:
i.e. noise is (short-term) stationary (+ ergodicity)
Hence noise(), σnoise2() can be estimated by averaging over noise-only frames
For each frame estimate clean speech spectrum Si() by using noisy speech spectrum Yi()
together with ^noise(), σ^noise2()
  based on `gain function’

## Slide 7: Spectral Subtraction: Basics
PS: Gain will be real-valued scalar between 0 and 1
    Only the magnitude of Yi(ω) is changed, noisy phase is unchanged
    Techniques for estimating clean phase also exist (details omitted)
PS: Applying a gain function as
    can improve signal-to-noise ratio (SNR) of the signal as a whole (i.e. in the time domain) but does not improve the SNR for a particular radial frequency (i.e. speech and noise are equally scaled)
    hence impact on speech intelligibility is found to be minimal (or non-existing) but ‘listening comfort’ is said to be improved
  For true SNR & speech intelligibility improvement, see multi-channel noise reduction (Chapter 3-4)

## Slide 8: Spectral Subtraction: Gain Functions
Examples
Magnitude Subtraction:
Spectral Subtraction:
Wiener Estimation:
Maximum Likelihood:
Ephraim-Malah: See next slide
(=most frequently used in practice)

## Slide 9: Spectral Subtraction: Gain Functions
Example 1: Ephraim-Malah Suppression Rule (EMSR)
with:
This corresponds to a MMSE (*) estimation of the ‘speech spectral amplitude’ |Si()| based on observation Yi() ( estimate equal to E{ |Si()| | Yi() } ) assuming Gaussian a priori distributions for Si() and Ni() [Ephraim & Malah 1984]
Similar formula for MMSE ‘log-spectral amplitude’ estimation [Ephraim & Malah 1985]
(*) minimum mean squared error
modified Bessel functions
skip formulas

## Slide 10: Spectral Subtraction: Gain Functions
Example 2: Magnitude Subtraction
  Signal model:
  Estimation of clean speech spectrum:
  PS: half-wave rectification
=‘instantaneous estimate’
(see also p.15)

## Slide 11: Spectral Subtraction: Gain Functions
Example 3: Wiener Estimation
  Linear MMSE estimation:
  find linear filter Gi() to minimize MSE
  Solution:
  Assume speech s[k] and noise n[k] are uncorrelated, then...
  PS: half-wave rectification
cross-correlation
auto-correlation
=‘instantaneous estimate’
(see also p.15)

## Slide 12: Overview
Frequency Domain Methods /
Spectral Subtraction Methods
  Spectral subtraction basics
  Gain functions
  Realization
  Musical noise
  Signal model based spectral subtraction
Time Domain Methods
  Kalman Filter Based Noise Reduction
  Subspace Methods

## Slide 13: Spectral Subtraction: Realization
Realization requires time-frequency analysis
(see DSP-CIS Chapter 14 on Short-Time Fourier Transform (STFT))
w[k] and v[k] = your favorite window functions
N = window length = DFT/DFT size = frequency resolution
D = window shift
yn[i] = n-th DFT output at time i = estimate for Y(n ) at time i (i-th frame)
G[n,i] = gain for n at time i (i-th frame)
yn[i]
y[k]
x
x
x
x
2
2
+
Example (N=4, D=2)
2
2
2
2
2
2

## Slide 14: Spectral Subtraction: Realization
This is a ‘Weigthed Overlap-Add’ (WOLA) Filter Bank (FB)
(see DSP-CIS Chapter 14)
w[k] and v[k] = prototype filters for DFT-modulated analysis/synthesis FB
N = number of filter bank channels
D = downsampling factor (e.g. 2-fold oversampling: D=N/2, 3-fold: D=N/3)
yn[i] = n-th subband signal
G[n,i] = subband processing in n-th subband
yn[i]
y[k]
2
2
x
x
x
x
2
2
+
Example (N=4, D=2)

## Slide 15: Spectral Subtraction: Musical Noise
Audio demo:
Artifact: musical noise
  What?
  Instantaneous/short-time estimates of |Yi()| fluctuate randomly
  resulting in random gains Gi()
  statistical analysis shows that broadband noise is transformed into signal composed of short-lived tones with randomly distributed frequencies (=musical noise)
magnitude subtraction

## Slide 16: Spectral Subtraction: Musical Noise
probability that speech is present, given observation
instantaneous
average
Solutions?
  Magnitude averaging: replace Yi() in calculation of Gi() by a local average over frames
  EMSR (see p.9)
  Augment Gi() with soft-decision VAD:
  Gi()  P(H1 | Yi()). Gi()
  …

## Slide 17: Overview
Frequency Domain Methods /
Spectral Subtraction Methods
  Spectral subtraction basics
  Gain functions
  Realization
  Musical noise
  Signal model based spectral subtraction
Time Domain Methods
  Kalman Filter Based Noise Reduction
  Subspace Methods

## Slide 18: Signal model based spectral subtraction
Basic:
Spectral subtraction with improved spectra estimation based on parametric speech signal model
Procedure:
  Estimate (initialize) parameters of speech model from noisy signal
  Using estimated parameters, perform noise reduction (e.g. Wiener estimation, p.11)
  Re-estimate parameters of speech model from the speech signal estimate
  Iterate 2 & 3

## Slide 19: Signal model based spectral subtraction
white noise
generator
pulse train
…
…
pitch period
voiced
unvoiced
x
Speech
signal
s[k]
frequency domain:
time domain:
= linear prediction (LP) parameters
all-pole filter
vs[k]

## Slide 20: Signal model based spectral subtraction
For each frame
      Estimate and (=time domain LP)
      Construct Wiener Filter (p.11)
        with:
        estimated from noise-only frames
      3. Apply Gi(ω)’s and obtain speech estimate (=time domain)
Repeat until
some error
criterion is
satisfied

## Slide 21: Overview
Frequency Domain Methods /
Spectral Subtraction Methods
  Spectral subtraction basics
  Gain functions
  Realization
  Musical noise
  Signal model based spectral subtraction
Time Domain Methods
  Kalman Filter Based Noise Reduction
  Subspace Methods

## Slide 22: Kalman Filter Recap 1/3
State space model of a time-varying discrete-time system
with v[k] and w[k]: mutually uncorrelated, zero mean, white noises
Then:
Given A[k], B[k], C[k], D[k], V[k], W[k] and
input/output-observations u[k],y[k], k=0,1,2,... then
Kalman filter produces MMSE estimates of internal states x[k], k=0,1,...
process noise
measurement
noise
Skip this slide

## Slide 23: Kalman Filter Recap 2/3
Definition: = MMSE-estimate of x[k] using all
available data up until time l
`FILTERING’ = estimate
`PREDICTION’ = estimate
`SMOOTHING’ = estimate
Skip this slide

## Slide 24: Kalman Filter Recap 3/3
Initalization:
‘Conventional’ Kalman Filter: For k=0,1,2,..
Given and corresponding error covariance matrix :
Step 1: Measurement Update
(produces ‘filtered’ estimate)
(compare to standard RLS!)
Step 2: Time Update
(produces ‘1-step prediction’)
 Better: ‘Square Root’ Algorithm (see DSP-CIS Chapter 14)
=error covariance matrix
PS: shorthand notation used here, i.e. xk, uk, Ak... instead of x[k], u[k],A[k],..
Skip this slide

## Slide 25: Kalman Filter Based Noise Reduction
Assume AR model of speech and noise
Equivalent state-space model is…
y[k] = microphone signal
vs[k], vn[k] = zero mean, unit
variance,white noise
Skip this slide

## Slide 26: Kalman Filter Based Noise Reduction
s[k] and n[k] are included in state vector, hence can be estimated
by a Kalman Filter (assuming α’s, β’s, … are known)
Skip this slide

## Slide 27: Kalman Filter Based Noise Reduction
Disadvantages:
  complexity
  delay
split signal
in frames
estimate
parameters
Kalman
Filter
reconstruct
signal
iterations for frame i
y[k]
Iterative algorithm (details omitted) (compare to p.20)
Frame i
Frame i
Skip this slide

## Slide 28: Kalman Filter Based Noise Reduction
State Estimator
(Kalman Filter)
Parameters Estimator
(Kalman Filter)
D
D
Sequential algorithm (details omitted)
Skip this slide

## Slide 29: Overview
Frequency Domain Methods /
Spectral Subtraction Methods
  Spectral subtraction basics
  Gain functions
  Realization
  Musical noise
  Signal model based spectral subtraction
Time Domain Methods
  Kalman Filter Based Noise Reduction
  Subspace Methods

## Slide 30: Subspace Methods
Signal model:
Construct Toeplitz matrix (LxM, L=N-M+1) :
  Hence: (with S and N similarly constructed)

## Slide 31: Subspace Methods
  Assumptions: Consider L>>M (‘tall thin’ matrices)
  Clean signal matrix S is rank deficient
  (e.g. ‘sum of sinusoids’ speech model)
  rank(S) = K < M
  Clean signal matrix S is orthogonal (≈uncorrelated) to noise
  (1/L) . ST N = 0
  White noise (see p.38 for coloured noise)
  (1/L) . NT N = 2noise .IM
  Assumptions better satisfied as L∞

## Slide 32: Subspace Methods
Tool: Singular value decomposition (SVD) of Y
  U is LxM orthogonal matrix UT.U=IMxM
  Columns of U are ‘left singular vectors’
  V is MxM orthogonal matrix VT.V=IMxM
  Columns of V are ‘right singular vectors’
  is MxM diagonal matrix
  Diagonal elements are ‘singular values’ i
  1 has K largest i corresponding to ‘signal+noise subspace’
  2 has M-K smallest I ≈noise corresponding to ‘noise subspace’
K=8
M=21
Singular value σi
i
Example

## Slide 33: Subspace Methods
Procedure
Step-1 : From SVD of Y, find estimate of S
  Least squares estimate
  Minimum variance estimate
Step-2 : Construct from

## Slide 34: Subspace Methods
Step-1 (v1.0) : Least squares estimator YLS
  Goal: approximate Y by a matrix YLS of rank K
  Solution is obtained by setting M-K smallest singular values to zero (`truncation’)
  Problem: proper determination of order K

## Slide 35: Subspace Methods
Step-1 (v2.0): Minimum variance estimator YMV
  Find a matrix T that minimizes
  (assume S is given, then i-th column of T
  is optimal linear filter for i-th column of S)
  Then:
PS : rank-deficiency condition not needed here
PS : 2noise has to be known (e.g. estimated during noise-only)
(*)

## Slide 36: Subspace Methods
Step-2 : Signal Reconstruction
Goal: Given , construct
Problem: does not have Toeplitz structure
Solution:
Restore Toeplitz structure by arithmetically averaging
every diagonal of the matrix
Hence:
(summation starts in column α)
(summation ends in column β)

## Slide 37: Subspace Methods
PS: Link with spectral subtraction?
  Compare (*) p.35 with gain function on p.11 (Wiener)
  Check that p.35-36 (for samples k=M,…,N-M+1) corresponds to
  which represents an analysis/synthesis filter bank with subband
  processing (be it without up/downsampling)
  Interpretation: Subspace method provides a ‘spectral subtraction’ in signal dependent filter bank (analysis filter bank VT, synthesis filter bank V) as an alternative to signal independent STFT/WOLA filter bank
+
s[k-3]
y[k]
^
M=4

## Slide 38: Subspace Methods
Audio Demo
Subspace Algorithm

## Slide 39: Subspace Methods
PS: What if coloured noise (1/L) .NT N  2noiseIM ?
  Estimate NTN during noise-only periods
  Similar procedure, now including ‘pre-whitening’ of Toeplitz matrix prior to SVD and ‘de-whitening’ step after estimation of
  Computational scheme can use ‘generalized SVD’ instead of SVD (with ‘built-in’ pre-/de-whitening)
  Easy, but details omitted…

## Slide 40: Conclusion
Many single-channel noise reduction
procedures available
Performance never spectacular
Seek performance improvement with
multi-channel processing (=Chapter 3-4)
PS: Recently strong shift towards machine learning based
single-channel noise reduction (not covered)