## Slide 1
Marc Moonen
Dept. E.E./ESAT-STADIUS, KU Leuven
marc.moonen@kuleuven.be
homes.esat.kuleuven.be/~moonen/
Digital Audio Signal Processing DASP Chapter-3:
Fixed Beamforming

## Slide 2: Overview
Introduction & beamforming basics
Data model & definitions
Filter-and-sum beamformer design
Matched filtering
  White noise gain maximization
  Ex: Delay-and-sum beamforming
Superdirective beamforming
  Directivity maximization
Directional microphones (delay-and-subtract)

## Slide 3: Introduction
Directivity pattern of a microphone
  A microphone (*) is characterized by a `directivity pattern which
  specifies the gain & phase shift that the microphone gives to a
  signal coming from a certain direction (i.e. `angle-of-arrival’)
  In general the directivity pattern is a function of frequency (ω)
  In a 3D scenario `angle-of-arrival’
  is azimuth + elevation angle
  Will consider only 2D scenarios for
  simplicity, with one angle-of arrival (θ),
  hence directivity pattern is H(ω,θ)
  (=angle-dependent transfer function)
  Directivity pattern is fixed and defined
  by physical microphone design
(*) We do digital signal processing, so this includes front-end filtering/A-to-D/..
|H(ω,θ)| for 1 frequency

## Slide 4: Introduction
Virtual directivity pattern of a microphone array
  By weighting or filtering (=freq. dependent weighting) and then summing signals from different microphones, a (software controlled) virtual directivity pattern (=weigthed sum of individual patterns) can be produced
(=FIR Filters)
+
:

## Slide 5: Introduction
This assumes all microphones receive the same signals (so must be in the same position)
However,
in a microphone array different microphones
are in different positions/locations
hence also receive different signals

## Slide 6: Introduction
+
:
Example : Uniform Linear Array (ULA)
Microphones placed on a line
Uniform inter-micr. distances (d)
Ideal micr. characteristics (Hm(ω,θ)=1)
For a far-field source signal
(i.e. plane wave), each microphone
receives the same signal, up
to an angle-dependent delay…
fs=sampling rate
c=propagation speed=343m/s

## Slide 7: Introduction
+
:
Beamforming = `spatial filtering’
based on
microphone characteristics (directivity patterns)
AND
microphone array configuration
(`spatial sampling’)

## Slide 8: Introduction
Classification:
  Fixed beamforming: data-independent, fixed filters Fm e.g. delay-and-sum, filter-and-sum
  Adaptive beamforming: data-dependent filters Fm e.g. LCMV-beamformer, generalized sidelobe canceler
=This chapter
=Next chapter
+
:

## Slide 9: Introduction
Background/history: ideas borrowed from antenna array design and processing for radar & (later) wireless communications
Microphone array processing considerably more difficult than antenna array processing:
  narrowband radio signals versus broadband audio signals
  far-field (plane waves) versus near-field (spherical waves)
  pure-delay environment versus multi-path environment
Applications: voice controlled systems (e.g. Xbox Kinect), speech communication systems, hearing aids,…

## Slide 10: Overview
Introduction & beamforming basics
Data model & definitions
Filter-and-sum beamformer design
Matched filtering
  White noise gain maximization
  Ex: Delay-and-sum beamforming
Superdirective beamforming
  Directivity maximization
Directional microphones (delay-and-subtract)

## Slide 11: Data model & definitions 1/5
Data model: source signal in far-field (see p.18 for near-field)
Microphone signals are filtered versions of source signal S() at angle 
Stack all microphone signals (m=1..M) in a vector
d is `steering vector’
Output signal after `filter-and-sum’ is
H instead of T for convenience (**)

## Slide 12: Data model & definitions 2/5
Data model: source signal in far-field
If all microphones have the same directivity pattern Ho(ω,θ), steering vector can be factored as…
Will often consider arrays with
ideal omni-directional microphones : Ho(ω,θ)=1
Example : uniform linear array, see p.6
Will use microphone-1 as reference (e.g. defining input SNR):
microphone-1 is used as a reference (=arbitrary)

## Slide 13: Data model & definitions 3/5
Definitions:
In a linear array (p.6) :  =90o=broadside direction
 = 0o =end-fire direction
Array directivity pattern (compare to p.3)
= `transfer function’ for source at angle  ( -π<< π )
Steering direction
= angle  with maximum amplification (for 1 freq.)
Beamwidth (BW)
= region around max with amplification > (max.amplif - 3dB) (for 1 freq.)

## Slide 14: Data model & definitions 4/5
Data model: source signal + noise
Microphone signals are corrupted by additive noise
Define noise correlation matrix as
Will assume noise field is homogeneous, i.e. all diagonal elements of noise correlation matrix are equal (=noise power spectrum) :
Then noise coherence matrix is

## Slide 15: Data model & definitions 5/5
Definitions:
Array Gain = improvement in SNR for source at angle  ( -π<< π )
Will consider 2 special cases...
|signal transfer function|^2
(with micr-1 used as reference: d1 =1)
|noise transfer function|^2

## Slide 16: Data model & definitions 5/5
Definitions:
Array Gain = improvement in SNR for source at angle  ( -π<< π )
White Noise Gain =array gain for spatially uncorrelated noise
(e.g. sensor noise)
ps: often used as a measure for robustness

## Slide 17: Data model & definitions 5/5
Definitions:
Array Gain = improvement in SNR for source at angle  ( -π<< π )
White Noise Gain =array gain for spatially uncorrelated noise
Directivity =array gain for diffuse noise (=coming from all directions)
DI(ω,max) and WNG(ω,max) used as performance criterion
..without proof
PS: ω is rad/sample ( -Π≤ω≤Π )
ω.fs is rad/sec
ω.fs/c = ..=2Π/λ is rad/meter
Zero-crossings at dj-di=(integer).λ/2
for λ=17m (@20Hz)..17mm(@20kHz)

## Slide 18: PS: Near-field beamforming
Far-field assumptions not valid for sources close to microphone array
  spherical waves instead of plane waves
  include attenuation of signals
  2 coordinates ,r (=position q) instead of 1 coordinate  (in 2D case)
Different steering vector (e.g. with Hm(ω,θ)=1 m=1..M) :
with q position of source
pref position of reference microphone pm position of mth microphone
e
e=1 (3D)…2 (2D)

## Slide 19: PS: Multipath propagation
In a multipath scenario, acoustic waves are reflected against walls, objects, etc..
Every reflection may be treated as a separate source (near-field or far-field)
A more realistic data model is then..
with q position of source and Hm(ω,q), complete transfer function from source position to m-the microphone (incl. micr. characteristic, position, and multipath propagation)
`Beamforming’ aspect vanishes here, see also Lecture-4
(`multi-channel noise reduction’)

## Slide 20: Overview
Introduction & beamforming basics
Data model & definitions
Filter-and-sum beamformer design
Matched filtering
  White noise gain maximization
  Ex: Delay-and-sum beamforming
Superdirective beamforming
  Directivity maximization
Directional microphones (delay-and-subtract)

## Slide 21: Filter-and-sum beamformer design
Basic: procedure based on page 13
(d(ω,θ) assumed known for all ω,θ)
(FIR Filters)
Array directivity pattern to be matched to given (desired) pattern
over frequency/angle range of interest
Non-linear optimization for FIR filter design (=ignore phase response)
Quadratic optimization for FIR filter design (=co-design phase response)

## Slide 22: Filter-and-sum beamformer design
Quadratic optimization for FIR filter design (continued)
  optimal solution is
Kronecker product

## Slide 23: Filter-and-sum beamformer design
Design example
M=8
Logarithmic array
N=50
fs=8 kHz

## Slide 24: Overview
Introduction & beamforming basics
Data model & definitions
Filter-and-sum beamformer design
Matched filtering
  White noise gain maximization
  Ex: Delay-and-sum beamforming
Superdirective beamforming
  Directivity maximization
Directional microphones (delay-and-subtract)

## Slide 25: Matched filtering: WNG maximization
Basic: procedure based on page 17
Maximize White Noise Gain (WNG) for given angle ψ
A priori knowledge/assumptions:
  angle-of-arrival ψ of source signal + corresponding steering vector
  noise scenario = white

## Slide 26: Matched filtering: WNG maximization
Maximization in
is equivalent to minimization of noise output power (under
white input noise), subject to unit response for angle ψ, i.e. (**)
Optimal solution (`matched filter’) is...
FIR approximation

## Slide 27: Matched filtering example: Delay-and-sum
Basic: Microphone signals are delayed and then summed together
Fractional delays implemented with truncated interpolation filters (=FIR)
Consider array with ideal omni-directional microphones
Then array can be steered to angle  :
Hence (for ideal omni-dir. micr.’s) this is matched filter solution

## Slide 28: Matched filtering example: Delay-and-sum
Array directivity pattern H(ω,θ):
=destructive interference
=constructive interference
White noise gain :
(independent of ω)
For ideal omni-dir. micr. array, delay-and-sum beamformer provides
WNG equal to M for all freqs (in the direction of steering direction ψ).
ideal omni-dir. micr.’s

## Slide 29: Matched filtering example: Delay-and-sum
Array directivity pattern H(,) for uniform linear array:
H(,) has sinc-like shape and is frequency-dependent
M=5 microphones
d=3 cm inter-microphone distance
=60 steering direction
fs=16 kHz sampling frequency
ideal omni-dir. micr.’s
=60
wavelength=4cm

## Slide 30: Matched filtering example: Delay-and-sum
Array directivity pattern H(,) for uniform linear array:
H(,) has sinc-like shape and is frequency-dependent
=endfire
=60
ideal omni-dir. micr.’s
wavelength=4cm

## Slide 31: Matched filtering example: Delay-and-sum
For an ambiguity, called spatial aliasing, occurs..
  This is analogous to time-domain aliasing where now the spatial sampling (=d) is too large.
Aliasing does not occur (for any ) if
ideal omni-dir. micr.’s
M=5 microphones
d=8 cm inter-microphone distance
=60 steering direction
fs=16 kHz sampling frequency

## Slide 32: Matched filtering example: Delay-and-sum
Ignore the
ideal omni-dir. micr.’s

## Slide 33: Matched filtering example: Delay-and-sum
Beamwidth for a uniform linear array:
hence large dependence on # microphones, distance (compare p.29 & 31) and frequency (e.g. BW infinitely large at DC) (compare to p.23)
Array topologies:
  Uniformly spaced arrays
  Nested (logarithmic) arrays (small d for high , large d for small )
  2D- (planar) / 3D-arrays
with e.g. =1/sqrt(2) (-3 dB)
ideal omni-dir. micr.’s

## Slide 34: Overview
Introduction & beamforming basics
Data model & definitions
Filter-and-sum beamformer design
Matched filtering
  White noise gain maximization
  Ex: Delay-and-sum beamforming
Superdirective beamforming
  Directivity maximization
Directional microphones (delay-and-subtract)

## Slide 35: Super-directive beamforming : DI maximization
Basic: procedure based on page 17
Maximize Directivity (DI) for given angle ψ
A priori knowledge/assumptions:
  angle-of-arrival ψ of source signal + corresponding steering vector
  noise scenario = diffuse

## Slide 36: Super-directive beamforming : DI maximization
Maximization in
is equivalent to minimization of noise output power (under
diffuse input noise), subject to unit response for angle ψ , i.e. (**)
Optimal solution (‘super-directive beamformer’) obtained as...
FIR approximation

## Slide 37: Super-directive beamforming : DI maximization
Directivity patterns for end-fire steering (ψ=0):
Superdirective beamformer has highest DI, but very poor WNG
(at low frequencies, where diffuse noise coherence matrix becomes ill-conditioned)
hence problems with robustness (e.g. sensor noise) !
M=5 d=3 cm
fs=16 kHz
Maximum directivity=M.M obtained for end-fire steering and for frequency->0 (without proof)
ideal omni-dir. micr.’s
WNG=M= 5
PS:
diffuse noise ≈
white noise for
high frequencies
(cfr. ωΠ and
c/fs=λmin/2≈min(dj-di)
in diffuse noise
coherence matrix)
DI=WNG=5
DI=M 2=25

## Slide 38: Overview
Introduction & beamforming basics
Data model & definitions
Filter-and-sum beamformer design
Matched filtering
  White noise gain maximization
  Ex: Delay-and-sum beamforming
Superdirective beamforming
  Directivity maximization
Directional microphones (delay-and-subtract)

## Slide 39: Differential microphones : Delay-and-subtract
First-order differential microphone = directional microphone
  2 closely spaced microphones, where one microphone signal is delayed
  (=hardware) and then subtracted from the other micropone signal
Array directivity pattern:
  First-order high-pass frequency dependence (jω)
  P() = freq.independent (!) directional response
  0  1  1 : P() is scaled cosine, shifted up with 1
  such that max = 0o (=end-fire) and P(max )=1
d/c <<,  <<
Continuous-time
system freq.resp.
ω = rad/sec

## Slide 40: Differential microphones : Delay-and-subtract
Types: dipole, cardioid, hypercardioid, supercardioid (HJ84)
=endfire
=broadside
Dipole:
1= 0 (=0) zero at 90o
DI=4.8dB
Cardioid:
1= 0.5 zero at 180o
DI=4.8dB
Supercardioid:
1=
zero at 125o,
DI=5.7 dB
highest front-to-back ratio
Hypercardioid:
1= 0.25
zero at 109o
highest DI=6.0dB