## Slide 1
Marc Moonen
Dept. E.E./ESAT-STADIUS, KU Leuven
marc.moonen@esat.kuleuven.be
homes.esat.kuleuven.be/~moonen/
Digital Audio Signal Processing DASP Chapter-4:
Adaptive Beamforming &
Multi-Channel Noise Reduction

## Slide 2: Overview
Recap
Adaptive Beamforming
  Adaptive beamforming goal & set-up
  LCMV beamformer
  Generalized sidelobe canceler
Multi-channel Wiener filter for multi-microphone noise reduction (/speech enhancement)
  Multi-microphone noise reduction problem
  Multi-channel Wiener filter (=spectral+spatial filtering)

## Slide 3: Recap 1/4
+
:
Filter-and-sum Beamforming
Classification:
  Fixed beamforming:
  Data-independent, fixed filters Fm e.g. matched filtering, superdirective, …
  Adaptive beamforming:
  Data-dependent filters Fm e.g. LCMV-beamformer, generalized sidelobe canceler
= This chapter
= Previous chapter

## Slide 4: Recap 2/4
Data model: source signal
Microphone signals are filtered versions of source signal S() at angle 
Stack all microphone signals (m=1..M) in a vector
d is `steering vector’

## Slide 5: Recap 3/4
Data model: source signal + noise
Microphone signals are also corrupted by additive noise
Noise correlation matrix is
Output signal after `filter-and-sum’ is

## Slide 6: Recap 4/4
Definitions:
Array directivity pattern = `transfer function’ for source signal at 
Array Gain = improvement in SNR for source signal at 
White Noise Gain
=array gain for spatially uncorrelated noise
Directivity
=array gain for diffuse noise

## Slide 7: Overview
Recap
Adaptive Beamforming
  Adaptive beamforming goal & set-up
  LCMV beamformer
  Generalized sidelobe canceler
Multi-channel Wiener filter for multi-microphone noise reduction (/speech enhancement)
  Multi-microphone noise reduction problem
  Multi-channel Wiener filter (=spectral+spatial filtering)

## Slide 8: Adaptive beamforming Goal & Set-up
Adaptive filter-and-sum structure:
  Aim is to minimize noise output power, while maintaining a fixed response for a given angle ψ (=assumed source signal angle) (plus possibly other linear constraints, see below)
  This is similar to the operation of a matched filter beamformer (in white noise) or superdirective beamformer (in diffuse noise) see Chapter-3 (**) p.26 & 36 but now noise field is unknown & adapted to
+
:

## Slide 9: Adaptive beamforming Goal & Set-up
Adaptive filter-and-sum structure:
  Will use (adaptive) FIR filters :
+
:

## Slide 10: Overview
Recap
Adaptive Beamforming
  Adaptive beamforming goal & set-up
  LCMV beamformer
  Generalized sidelobe canceler
Multi-channel Wiener filter for multi-microphone noise reduction (/speech enhancement)
  Multi-microphone noise reduction problem
  Multi-channel Wiener filter (=spectral+spatial filtering)

## Slide 11: LCMV beamformer
LCMV = Linearly Constrained Minimum Variance
  Minimize (source signal+noise) output power (=‘variance’) z[k] (see ‘Note’) :
  Subject to (J) linear constraints to avoid source signal cancellation
    Example: fix array directivity pattern for angle ψ at J sample freqs ωi
Note: For J∞, constrained output power minimization corresponds to constrained noise output power minimization (if source signal angle is equal to ψ). (why?)
Hence, this LCMV formulation is appropriate for cases where Ryy can be estimated, while Rnn can not be estimated separately.
When the source signal is a speech signal, where Rnn is observable during speech pauses, then Rnn can be used instead of Ryy in the LCMV formulation (see p.21).

## Slide 12: LCMV beamformer
LCMV = Linearly Constrained Minimum Variance
  Minimize output power z[k]:
  Subject to (J) linear constraints to avoid source signal cancellation
  Solution is (obtained using Lagrange-multipliers, etc..):
  This can be computed for each time k: first estimate Ryy-1[k], etc..
  But would rather have a truly recursive algorithm, see next slides
  PS: Compare to Chapter-3, p.26 & 36 (frequency domain & J=1, RnnRyy)

## Slide 13: Overview
Recap
Adaptive Beamforming
  Adaptive beamforming goal & set-up
  LCMV beamformer
  Generalized sidelobe canceler
Multi-channel Wiener filter for multi-microphone noise reduction (/speech enhancement)
  Multi-microphone noise reduction problem
  Multi-channel Wiener filter (=spectral+spatial filtering)

## Slide 14: Generalized sidelobe canceler (GSC)
GSC = Adaptive filter solution for LCMV-problem
Constrained optimisation is reformulated as a constraint pre-processing,
followed by an unconstrained optimisation, as follows:
  LCMV-problem is
  Define `blocking matrix’ Ca,, columns spanning the null-space of C
  Define ‘quiescent response vector’ fq satisfying constraints
  Parametrize all f’s that satisfy constraints (verify!)
  i.e. filter f can be decomposed in a fixed part fq and a variable part Ca. fa

## Slide 15: Generalized sidelobe canceler (GSC)
GSC = Adaptive filter formulation of the LCMV-problem
Constrained optimisation is reformulated as a constraint pre-processing,
followed by an unconstrained optimisation, as follows:
  LCMV-problem is
  Unconstrained optimization of fa :
  (MN-J coefficients)

## Slide 16: Generalized sidelobe canceler
GSC (continued)
  Hence unconstrained optimization of fa can be implemented as an
  adaptive filter (adaptive linear combiner), with filter inputs (=‘left-
  hand sides’) equal to and desired filter output (=‘right-hand side’) equal to
  Example: LMS algorithm

## Slide 17: Generalized sidelobe canceler
GSC then consists of three parts:
Fixed beamformer (cfr. fq ), satisfying constraints (‘LC’) but not yet minimum variance (‘MV’) ), creating `source signal reference’
Blocking matrix (cfr. Ca), beamformers with null response for angle ψ (at sampling frequencies) (cfr. C’.Ca=0), creating MN-J `noise references’
Multi-channel adaptive filter
(linear combiner)
your favourite one, e.g. LMS
PS: = large matrix
complexity O(MN.(MN-J))
even with LMS for fa

## Slide 18: Generalized sidelobe canceler
A popular & cheaper GSC realization is as follows
Note that some reorganization has been done:
The blocking matrix now generates (typically) M-1 (instead of MN-J) noise references.
The multichannel adaptive filter performs FIR-filtering on each noise reference (instead of merely scaling in the linear combiner) (=complexity O((M-1)N) for LMS)
Philosophy is the same, mathematics are different (details on next slide).
Postproc
y1
yM
ignore
ignore
ignore

## Slide 19: Generalized sidelobe canceler
A popular & cheaper GSC realization is as follows (continued)
Blocking matrix
  Creating (M-1) independent noise references by means of (M-1) beamformers with null response for angle ψ
  Different possibilities, e.g.
(ψ=90 , i.e. ‘broadside steering’)
Griffiths-Jim
Walsh

## Slide 20: Generalized sidelobe canceler
Math details: (ψ=90 , i.e. ‘broadside steering’)
=input to multi-channel adaptive filter
select `sparse’ blocking matrix such that :
=use this as blocking matrix now

## Slide 21: Generalized sidelobe canceler
Problems of GSC:
  Impossible to reduce noise from angle ψ (cfr. constraint)
  If steering vectors d(ωi,ψ) (see p.11) are not accurately known (e.g. due to inaccurate source position or reverberation), will have source signal ‘leakage’ into noise references, which can lead to source signal cancellation by the adaptive filter.
  Therefore, to avoid source signal cancellation, adaptive filter should
  only be updated when no source signal is present
  (i.e. in noise-only periods).
  In speech applications, this is done with a
  voice activity detection (VAD).
  Effectively, this corresponds to replacing Ryy by Rnn in p.11 (and
  following slides)

## Slide 22: Overview
Recap
Adaptive Beamforming
  Adaptive beamforming goal & set-up
  LCMV beamformer
  Generalized sidelobe canceler
Multi-channel Wiener filter for multi-microphone noise reduction (/speech enhancement)
  Multi-microphone noise reduction problem
  Multi-channel Wiener filter (=spectral+spatial filtering)

## Slide 23: Multi-Microphone Noise Reduction Problem
(some) speech estimate
speech source
noise source(s)
microphone signals
?
speech part
noise part
M= number of microphones
compare to Chapter-2

## Slide 24: Multi-Microphone Noise Reduction Problem
Will estimate speech
part in microphone 1
(*) (**)
?
(*) Estimating s[k] is more difficult, would include dereverberation
(**) This is similar to single-microphone model (Chapter-2), where additional
microphones (m=2..M) help to get a better estimate

## Slide 25: Multi-Microphone Noise Reduction Problem
Data model:
(frequency domain)
See Chapter-3 on multi-path propagation (with q left out for conciseness)
Hm(ω) is complete transfer function from speech source position to m-the microphone
No prior knowledge assumed here!

## Slide 26: Overview
Recap
Adaptive Beamforming
  Adaptive beamforming goal & set-up
  LCMV beamformer
  Generalized sidelobe canceler
Multi-channel Wiener filter for multi-microphone noise reduction (/speech enhancement)
  Multi-microphone noise reduction problem
  Multi-channel Wiener filter (=spectral+spatial filtering)

## Slide 27: Multi-Channel Wiener Filter (MWF)
Data model:
Will use linear filters to obtain speech estimate
Wiener filter (=linear MMSE approach)
Note that (unlike in DSP-CIS) `desired response’ signal S1(w) is unknown here (!)

## Slide 28: Multi-Channel Wiener Filter (MWF)
Wiener filter solution is (see DSP-CIS)
  All quantities can be estimated !
  Special case of this is single-channel Wiener filter formula (Chapter-2)
  In practice, use alternative to ‘subtraction’ operation (see slide 32)
compute during speech+noise periods
compute during noise-only periods

## Slide 29: Multi-Channel Wiener Filter (MWF)
MWF combines spatial filtering with
single-channel spectral filtering (as in Chapter-2) :
if
then…

## Slide 30: Multi-Channel Wiener Filter (MWF)
…then it can be shown that
represents a spatial filtering (*)
  Compare to superdirective & matched filter beamforming (Chapter-3)
  Matched filter beamf. maximizes array gain in white noise field
  Superdirective beamf. maximizes array gain in diffuse noise field
  MWF maximizes array gain in unknown (!) noise field.
  MWF is operated without invoking any prior knowledge (steering
  vector/noise field) ! (the secret is in the voice activity detection… (explain))
(*) Note that spatial filtering can improve SNR, spectral filtering never improves SNR
(at one frequency)

## Slide 31: Multi-Channel Wiener Filter (MWF)
…then it can be shown that
represents a spatial filtering (*)
represents an additional spectral ‘post-filter’
  i.e. single-channel Wiener estimate of S1(ω) (Chapter-2 p.9) applied to output signal of spatial filter (...prove it!)

## Slide 32: Multi-Channel Wiener Filter (MWF)
Correlation matrices
  are estimated in each frame by averaging over a number of previous frames, possibly with exponential weighting, i.e.
Update in speech+noise frames
Update in noise-only frames

## Slide 33: Multi-Channel Wiener Filter (MWF)
Note that (in the above formula)
is a positive-definite rank-1 matrix, whereas (with estimated matrices)
is generally not rank-1, and often not positive-definite
Hence
generally provides a poor filter estimate..

## Slide 34: Multi-Channel Wiener Filter (MWF)
A better procedure (v1.0) could be as follows
where ϕspeech is a rank-1 matrix estimated (in each frame) as

## Slide 35: Multi-Channel Wiener Filter (MWF)
An even better procedure (v2.0) is as follows
where ϕspeech is a rank-1 matrix estimated (in each frame) as
which now also includes a ‘noise whitening’ operation
(making the estimation also immune to, for instance, scalings of the microphone signals)

## Slide 36: Multi-Channel Wiener Filter (MWF)
Solution is (for v2.0) is based on
Generalized Eigenvalue Decomposition
of matrix pair {ϕ^s&n, ϕ^noise} :
a.k.a
‘joint diagonalization’

## Slide 37: Multi-Channel Wiener Filter (MWF)
With this ϕspeech (in v2.0) becomes (proof omitted)
and then
PS: If kth microphone is reference microphone (instead of 1st microphone, see page 24) then first line has ek, last line has [QH]1k and e1

## Slide 38: Multi-Channel Wiener Filter (MWF)
Scalar is representative of spectral filtering:
Compare with spectral subtraction formulas…
Eigenvalues (σs&n/σnoise) represent signal-to-noise ratios
Eigenvector is representative of spatial filtering:
Compare to p.30-31

## Slide 39: Multi-Channel Wiener Filter: Implementation
Implementation with short-time Fourier transform (see Chapter-2)
Implementation with time-domain FIR filtering:
filter
coefficients

## Slide 40: Multi-Channel Wiener Filter: Implementation
Solution is…
compute during speech+noise periods
compute during noise-only periods
Implementation with time-domain linear filtering: