## Slide 1
Marc Moonen
Dept. E.E./ESAT-STADIUS, KU Leuven
marc.moonen@kuleuven.be
homes.esat.kuleuven.be/~moonen/
Digital Audio Signal Processing DASP Chapter-5:
Acoustic Echo & Feedback Cancellation

## Slide 2: Outline
Acoustic Echo Cancellation (AEC)
Intro/Acoustic Channels
Adaptive Filters for AEC
Control Algorithm
Stereo AEC
Acoustic Feedback Control (AFC)
Intro/Nyquist Stability & Maximum Stable Gain
AFC Methods
Notch-Filter-Based Howling Suppression (NHS)
Adaptive Feedback Cancellation (AFC)

## Slide 3: Introduction
Acoustic Echo Cancellation (AEC)
Suppress echo..
  To guarantee normal conversation conditions
  To prevent the closed-loop system from becoming unstable
Applications
  Teleconferencing
  Hands-free telephony
  Handsets, ..

## Slide 4: Introduction: Acoustic Channels
Loudspeaker + acoustic path + microphone can be modeled with sufficient accuracy as a linear filtering operation
PS: Loudspeaker often introduces non-linear distortion,
not taken into account here
Acoustic path is represented by the
acoustic impulse response
  First there is a dead time. Then come the direct path impulse and some early reflections, which depend on the geometry of the room. Finally there is an exponentially decaying tail called reverberation, coming from multiple reflections on walls, objects,... Reverberation mainly depends on ‘reflectivity’ (rather than geometry) of the room…

## Slide 5: Introduction: Acoustic Channels
To characterize the ‘reflectivity’ of a room the reverberation
time ‘RT60’ is defined
  RT60 = time which the sound pressure level or intensity needs
  to decay to -60dB of its original value
  For a typical office room RT60 is between 100 and 400 ms, for a church RT60 can be several seconds
PS: Acoustic room impulse responses are highly time-varying !!!!
PS: Acoustic room impulse responses are position dependent !!!!
ESAT speech laboratory
RT60  120 ms
Begijnhofkerk Leuven
RT60  3730 ms

## Slide 6: Acoustic Channels
Acoustic Impulse Response : FIR or IIR ?
If the acoustic impulse response is modeled as an..
  FIR filter  hundreds/thousands of filter taps are needed
  IIR filter  filter order can be reduced, but still hundreds of filter
  coeffs (num. + denom.) may be needed (sigh!)
Furthermore...
  In a speech comms set-up the acoustics are highly time-varying, hence adaptive filtering techniques are called for (see DSP-CIS):
    FIR adaptive filters : simple adaptation rules, no local minima,..
    IIR adaptive filters : more complex adaptation, local minima, have to monitor stability, ..
Hence FIR models are used in practice

## Slide 7: Outline
Acoustic Echo Cancellation (AEC)
Intro/Acoustic channels
Adaptive filters for AEC
Control Algorithm
Stereo AEC
Acoustic Feedback Control (AFC)
Intro/Nyquist Stability & Maximum Stable Gain
AFC Methods
Notch-Filter-Based Howling Suppression (NHS)
Adaptive Feedback Cancellation (AFC)

## Slide 8: Adaptive filters for AEC
Basic set-up
Adaptive filter produces a model for acoustic room impulse response +
an estimate of the echo contribution in microphone signal, which is
then subtracted from the microphone signal
Thanks to adaptivity
  time-varying acoustics can be tracked
  performance superior to performance of `conventional’ techniques (e.g. voice controlled switching, loss control, etc.)

## Slide 9: Adaptive filters for AEC: NLMS
NLMS update equations
in which
N is # filter taps, k is the discrete-time index
 is the adaptation stepsize and  is a regularization parameter

## Slide 10: Adaptive filters for AEC: NLMS
Pros and cons of NLMS
  + cheap algorithm : O(N)
  + small input/output delay (= 1 sample)
  for colored far-end signals (such as speech) convergence of the NLMS algorithm is slow
  (cfr λmax versus λmin, etc…., see DSP-CIS)
  large N then means even slower convergence
  ¤ NLMS is thus often used for the cancellation of short echo paths

## Slide 11: Adaptive filters for AEC
As some input/output delay is acceptable in AEC (e.g. ITU says 16ms), algorithms can be derived that are even cheaper than NLMS, by exchanging implementation cost for extra processing delay, sometimes even with improved performance :
    Frequency-domain adaptive filtering (FDAF)
    Partitioned Block FDAF (PB-FDAF)
+ cost reduction
+ optimal (stepsize) tuning for each subband/frequency bin
separately results in improved performance

## Slide 12: Adaptive filters for AEC: Block-LMS
To derive the frequency-domain adaptive filter the BLMS algorithm is considered first
in which
N is # filter taps, L is block length, n is block time index
BLMS = gradient averaging over block of L samples (i.o. 1 sample in LMS)

## Slide 13: Adaptive filters for AEC: Block-LMS
Both the BLMS convolution and correlation operation are computationally demanding. They can be implemented more efficiently in the frequency domain using fast convolution techniques, i.e. overlap-save/overlap-add :
with
M-point DFT-matrix
convolution
correlation
overlap-save

## Slide 14: Adaptive filters for AEC: FDAF
Overlap-save FDAF
Will only work if
(M is DFT-size)

## Slide 15: Adaptive filters for AEC: FDAF
¤ Typical parameter setting for the FDAF :
¤ FDAF is functionally equivalent to BLMS (!)
+ FDAF is significantly cheaper than (B)LMS (cfr FFT/IFFT i.o. DFT/IDFT)
for a typical parameter setting If N=1024 :
- Input/output delay is equal to 2L-1=2N-1, which may be unacceptably large for realistic parameter settings : e.g. if N=1024 and fs=8000Hz  delay is 256 ms !

## Slide 16: Adaptive filters for AEC: PB-FDAF
Overlap-save PB-FDAF : N-tap filter split into (N/P) filter sections, P-taps each, then apply overlap-save to each section
(`P takes the place of N’).
Will only work if

## Slide 17: Adaptive filters for AEC: PB-FDAF
¤ Typical parameter setting :
¤ PB-FDAF is intermediate between LMS and FDAF (N/P=1)
¤ PB-FDAF is functionally equivalent to BLMS
+ PB-FDAF is cheaper than (B)LMS :
If N=1024, P=L=128, M=256 
+ Input/output delay is 2L-1 which can be chosen small, in the example above the delay is 32 ms, if fs=8000Hz
+ Instead of a simple stepsize , ‘subband’ dependent stepsizes i can be applied to increase convergence speed
¤ used in commercial AECs

## Slide 18: Outline
Acoustic Echo Cancellation (AEC)
Intro/Acoustic channels
Adaptive filters for AEC
Control Algorithm
Stereo AEC
Acoustic Feedback Control (AFC)
Intro/Nyquist Stability & Maximum Stable Gain
AFC Methods
Notch-Filter-Based Howling Suppression (NHS)
Adaptive Feedback Cancellation (AFC)

## Slide 19: Control Algorithm
Adaptation speed ( ) in LMS-type algorithms should be adjusted…
  to the far-end signal power, in order to avoid instability of the adaptive filter (see DSP-CIS)  stepsize normalization (e.g. NLMS)
  to the amount of near-end activity, in order to prevent the filter to move away from the optimal solution (see DSP-CIS on ‘excess MSE’)
   double-talk detection
Double talk refers to the situation where both the far-end and the
near-end speaker are active.

## Slide 20: Control Algorithm
3 modes of operation:
    Near-end activity (single or double talk) (Ed large) 
    No near-end activity, only far-end activity (Ex large, Ed small) 
    No near-end activity, no far-end activity (Ex small, Ed small) 
 FILT+ADAPT
 FILT
 NOP
Ex is short-time energy of
the far-end signal (loudspeaker)
Ed is short-time energy of
the desired signal (microphone)

## Slide 21: Control Algorithm
Double-talk Detection (DTD)
Problem: detection of (near-end) speech during (far-end) speech
Desired properties: Limited number of false alarms, small delay, low complexity, etc...
Different approaches exist, which are based on energy, correlation, spectral contents, etc…
Example: Energy-based DTD
  Method-1
  If Ed >  Ex  double talk ( is a chosen threshold)
  Method-2
If  > 1  double talk (with )

## Slide 22: Outline
Acoustic Echo Cancellation (AEC)
Intro/Acoustic channels
Adaptive filters for AEC
Control Algorithm
Stereo AEC
Acoustic Feedback Control (AFC)
Intro/Nyquist Stability & Maximum Stable Gain
AFC Methods
Notch-Filter-Based Howling Suppression (NHS)
Adaptive Feedback Cancellation (AFC)

## Slide 23: Stereo-AEC
Mono : autocorrelation of x-signal (e.g. speech) has
an impact on convergence (see DSP-CIS)
Stereo : also cross-correlation between signals x1 and x2
plays a role now…
Stereo-AEC Conditioning Problem:
S-AEC input vectors are
 Large(r) eigenvalue spread (λmax>> λmin,, i.e. large(r) condition number)
of correlation matrix -> large(r) impact on convergence !

## Slide 24: Stereo-AEC
Hence filter input correlation matrix will be rank-deficient
(with `null-space’, hence λmin=0, hence worst possible (∞) eigenvalue spread)
Hence LMS converges to a filter vector with spurious contribution
α.[G2T -G1T]T (corresponding to non-converging ‘mode’ defined by λmin) , which depends
on transmission room, i.e. G1 & G2, which themselves are time-varying!
Stereo-AEC Conditioning Problem:
Consider transmission room
impulse responses G1,G2 (length Q)
Assume then :
explain!

## Slide 25: Stereo-AEC
In practice :
So that correlation matrix will be (only) ill-conditioned
(instead of rank-deficient)
…which however is still bad news
Hence

## Slide 26: Stereo-AEC
Reduce correlation between the loudspeaker signals by…
  Complementary comb filters
  White noise insertion
  Colored (masked) noise insertion (p27)
  Non-linear processing (p28)
Disadvantages :
  Signal distortion
  Stereo perception may be affected
- In addition : use algorithms that are less sensitive to the
condition number than NLMS, e.g. RLS, ...
Comb-1 for x1, comb-2 for x2
Stereo-AEC Fixes:

## Slide 27: Stereo-AEC
Remove all signal content below the masking threshold
Fill with noise (both channels independently)
Correlation between input channels decreases
Poor performance for speech
Good performance for music
Computationally intensive
Stereo-AEC Fixes:
Colored noise insertion

## Slide 28: Stereo-AEC
is often a half wave rectifier
is necessary for good performance, but audible
Good results for speech, audible artifacts in music
Stereo-AEC Fixes:
Non-linear processsing

## Slide 29: Outline
Acoustic Echo Cancellation (AEC)
Intro/Acoustic channels
Adaptive filters for AEC
Control Algorithm
Stereo AEC
Acoustic Feedback Control (AFC) (*)
Intro/Nyquist Stability & Maximum Stable Gain
AFC Methods
Notch-Filter-Based Howling Suppression (NHS)
Adaptive Feedback Cancellation (AFC)
(*) Reference: T. van Waterschoot & M. Moonen, “Fifty years of acoustic feedback control: state of the art and future challenges,” Proc. IEEE, vol. 99, no. 2, 2011, pp. 288-327.

## Slide 30: Introduction
Acoustic Feedback Control (AFC)
Single channel AFC =
- One loudspeaker
- One microphone
Multi-channel AFC = ………..
(not treated here)
Applications
  Hearing aids
  Sound reinforcement

## Slide 31: AFC Basics
“Desired” system transfer function:
Closed-loop system transfer function:
  Spectral coloration
  Acoustic echoes
  Risk of instability
Loop response:
  Loop gain
  Loop phase

## Slide 32: AFC Basics
Nyquist stability criterion:
  If there exists a radial frequency ω for which
  then the closed-loop system is unstable
  If the unstable system is excited at the critical frequency ω, then an oscillation at this frequency will occur = howling
Maximum stable gain (MSG):
  Maximum forward path gain before instability
  Desirable gain margin 2-3 dB (= MSG – actual forward path gain)
if G has flat response
[Schroeder, 1964]
B=bandwidth

## Slide 33: AFC Methods
Phase modulation (PM) methods (not addressed here)
  Apply frequency/phase modulations in forward path
Spatial filtering methods
  Microphone beamforming to reduce direct coupling
  (Lecture 2)
Gain reduction methods
  (Frequency-dependent) gain reduction after howling detection
  Example: Notch-filter-based howling suppression (NHS)
Room modeling methods
  Adaptive inverse filtering (AIF): adaptive equalization of acoustic feedback path response (not addressed here)
  Adaptive feedback cancellation (AFC): adaptive prediction and subtraction of feedback component in microphone signal
Skip this slide

## Slide 34: Notch-Filter-Based Howling Suppression (NHS)
Gain reduction after howling detection
NHS subproblems:
  Howling detection
  Notch filter design
Skip this slide

## Slide 35: Notch-Filter-Based Howling Suppression (NHS)
Skip this slide

## Slide 36: Notch-Filter-Based Howling Suppression (NHS)
Skip this slide

## Slide 37: Adaptive Feedback Cancellation (AFC)
Predict and subtract entire feedback signal (i.o. only howling component) in microphone signal
Requires adaptive estimation of acoustic feedback path model
Similar to AEC, but more difficult due to closed signal loop
(-> correlation of loudspeaker
and source signal

## Slide 38: Adaptive Feedback Cancellation (AFC)
AFC correlation problem
  Optimal filter (Wiener filter) will have
  a non-zero bias
  Non-zero bias results in (partial) source signal (v) cancellation
Need decorrelation of loudspeaker and source signal
WF

## Slide 39: Adaptive Feedback Cancellation (AFC)
Two methods…
1. Decorrelation in the signal loop
  Noise injection 
  Time-varying processing
  Nonlinear processing
  Forward path delay
Inherent trade-off
between decorrelation
and sound quality

## Slide 40: Adaptive Feedback Cancellation (AFC)
2. Decorrelation in the adaptive filtering circuit
  Decorrelating prefilters to remove bias in adaptive filter
  based on source signal model
Sound quality not compromised
Prediction-error-method (PEM)
(details omitted)
  joint estimation of acoustic feedback path and source signal model
  25-50% computational overhead compared to standard ad.filtering algorithms
leads to unbiased
estimate !