## Slide 1: Digital Audio Signal Processing DASP Chapter-6: Sound Field Control
Jesper Brunnström - Marc Moonen
Dept. E.E./ESAT-STADIUS, KU Leuven
marc.moonen@kuleuven.be
homes.esat.kuleuven.be/~moonen/

## Slide 2: Sound field control - Outline
www.harman.com
www.silentium.com
Basics
  Signal Model
Sound zone control
  Pressure Matching
  Acoustic Contrast Control
Active noise control
  Feedforward ANC
  Filtered-x LMS
  Feedback ANC

## Slide 3: Basics
Design loudspeaker signal(s) from
reference signal(s), to control sound
at some point(s) in a room/space
Reference signal(s) either given
or recorded (microphone(s))
Requires knowledge of acoustic
impulses responses from each
loudspeaker to each control point (microphone)
  Acoustic impulse responses may be measured
  ahead of time (’calibration’)
  Calibration can be a difficult in practice, time
  consuming, or problematic if system is time-varying
Example: Binaural synthesis

## Slide 4: Basics
Example: Binaural synthesis
virtual
sound source
…
…
…
…
Example: Sound field synthesis based on Huygens’ principle

## Slide 5: Basics - Signal model
Sound pressure at a control point resulting from a single loudspeaker is..
Loudspeaker signal is reference/input signal filtered by control filter
Loudspeaker signal
Acoustic path
Acoustic path is generally modelled as a linear finite impulse response filter
Reference signal
Control filter

## Slide 6: Basics - Signal model
Matrix form: w and h commute if time-invariant
= linear function of w

## Slide 7: Sound field control - Outline
www.harman.com
www.silentium.com
Basics
  Signal Model
Sound zone control
  Pressure Matching
  Acoustic Contrast Control
Active noise control
  Feedforward ANC
  Filtered-x LMS
  Feedback ANC

## Slide 8: Sound zone control – Problem statement
Solve with superposition
  Hence can consider problem with only a single input/reference signal, a single ’bright zone’, all other zones are ’dark zones’
Reproduce different sounds for different listeners in the same room/space, with minimal interference
Bright zone: Reproduce input signal Dark zone: Quiet
Other spaces: Any sound
Acoustic impulse responses from all loudspeakers to a dense set of control points (microphones) in all zones assumed given
Can be viewed as ’transmit beamforming’ (vs. ’receive beamforming in Chapter 3-4)

## Slide 9: Sound zone control – Signal model
One input signal x(n) (cfr. superposition)
One control filter per loudspeaker
One acoustic path from each loudspeaker to each control point (microphone)
Sound pressure at m-th
control point (microphone)
Acoustic impulse response
from l-th loudspeaker to
m-th control point (microphone)
Control filter for
l-th loudspeaker
ml

## Slide 10: Sound zone control – Signal model
Matrix form:
Acoustic paths from all (L) loudspeakers to all (Mb) microphones in bright zone
Stack control filters for all loudspeakers
Block diagonal matrix with duplicated signal vectors
T
T
Sound pressure in Mb bright
zone microphones
Similarly:
Sound pressure in Md dark
zone microphones

## Slide 11: Sound zone control - Pressure Matching
Minimize the mean squared error (MSE) between the desired and reproduced signal
Desired signal in dark zones is 0
Optimal filters computed by setting gradient to zero...
Desired signal in bright zone is usually input signal as reproduced by a virtual source

## Slide 12: Sound zone control - Pressure Matching
Correlation matrices are defined in terms of known signal and acoustic impulse responses, hence can be computed ahead of operation
MSE-optimal control filters are
with

## Slide 13: Sound zone control - Pressure Matching
Same principles as for GEVD-based multichannel Wiener filter can be applied
Simultaneous diagonalization of matrix pair {Rb,Rd} is
then
T. Lee, J. K. Nielsen, J. R. Jensen, and M. G. Christensen, ‘A unified approach to generating sound zones using variable span linear filters’,
2018 IEEE International Conference on Acoustics, Speech and Signal Processing (ICASSP), Calgary, Canada, Apr. 2018, pp. 491–495.
Skip this slide

## Slide 14: Sound zone control – Acoustic Contrast Control
Approximate with the R largest eigenvalues/eigenvectors
Trade-off...
- Full rank gives lowest error in the bright & dark zone (cfr. MSE)
- Rank-1 gives highest ’acoustic contrast’, i.e. ratio of signal
power in bright zone to signal power in dark zones (no proof)
= Acoustic Contrast Control (ACC)
r-th column of U
r-th diagonal element of Λ
T. Lee, J. K. Nielsen, J. R. Jensen, and M. G. Christensen, ‘A unified approach to generating sound zones using variable span linear filters’,
2018 IEEE International Conference on Acoustics, Speech and Signal Processing (ICASSP), Calgary, Canada, Apr. 2018, pp. 491–495.
Skip this slide

## Slide 15: Sound field control - Outline
www.harman.com
www.silentium.com
Basics
  Signal Model
Sound zone control
  Pressure Matching
  Acoustic Contrast Control
Active noise control
  Feedforward ANC
  Filtered-x LMS
  Feedback ANC

## Slide 16: Active Noise Control - Intro
Passive noise control : sound absorbers, …
works well only for high frequencies (`centimeter-waves’)
Active noise control : for low frequencies (e.g. 100 Hz  λ=3,4m)
  General set-up
ANC works on the principle of destructive interference between the sound field generated by the `primary’ (noise) source and the sound field due to secondary source(s), whose output can be controlled
Aim: generate `quiet’
at error microphone

## Slide 17: Active Noise Control - Intro
PS: Destructive interference relies on superposition & linearity
  At higher volume, loudspeaker can exhibit non-linear behavour
After destructive interference at main frequency, harmonics
generated by loudspeaker may become distinctly audible
Non-linearity not considered here
PS: Destructive interference at
one point, may imply
constructive interference
at other point
  Secondary source to be placed close to error microphone, so that only
  modest secondary signal is required, and hence points further away
  from secondary source are not affected. Produce `zone of quiet’ near
  the error microphone (e.g. 10dB reduction in zone approx λ/10)

## Slide 18: Feedforward ANC
Basic set-up
  P(z) = primary path = unknown
  H(z) = secondary path = acoustic path from loudspeaker (=secondary source) to error microphone.
  H(z) can be modeled/identified (=calibration)
  Secondary signal at error microphone is ideally equal to –d(n)
  However (unlike in sound zoning): d(n) is not known/observed, only e(n) is observed…
H(z)
d
e
W(z)
y
secondary
path
primary
source
x
P(z)

## Slide 19: Feedforward ANC
Basic set-up
(continued)
  However (unlike in sound zoning): d(n) is not known/observed, only e(n) is observed…
  Hence need adaptive filter controlled by e(n)
  Design adaptive filter W(z) to minimize MSE (compare to AEC!)
H(z)
d
e
W(z)
y
secondary
path
primary
source
x
P(z)

## Slide 20: Feedforward ANC
Signal model
Reference signal is input to the control filter
(must be correlated with the primary signal)
Error microphone signal
Secondary signal
Primary (unwanted) signal
Control
filter
Reference signal
Secondary path
See page 5
= correct if w & h are time-invariant
= approximation if w is (slowly)
time-varying (cfr infra)

## Slide 21: Feedforward ANC
Correlation between the error signal e(n)
and the reference signal x(n) filtered through the secondary path h, i.e.
Minimize MSE cost function
2

## Slide 22: Feedforward ANC – Filtered-x LMS
Gradient descent adaptive filter
Stochastic gradient adaptive filter
  uses instantaneous estimate of gradient ( = LMS (Least Mean Squares))
Step size
Gradient is the direction in which the function increases fastest
Change the control filter in small steps in the opposite direction
This is referred to as ’Filtered-x LMS’
..as the input signal x(n) is first filtered by the secondary path h

## Slide 23: PS: Interpretation
  Straightforward application of LMS :
  …does not work here
  (ex.: H(z)=-1, then steepest descent turned into steepest ascent)
H(z)
d
e
W(z)
y
secondary
path
primary
source
x
P(z)

## Slide 24: PS: Interpretation
  This would have been a simpler problem (swap H and W)…
  ...allowing for straightforward application of LMS, with filtered x-signal
  PS: Again, only time-invariant linear systems commute, hence (implicit) swapping will require slow adaptation of W(z)
H(z)
d
e
W(z)
y
x
P(z)

## Slide 25: PS: Interpretation
  Filtered-X LMS scheme : swapping of H and W only in adaptation path (not in filtering path)
  …with in practice H’(z) an estimate of H(z)
H(z)
d
e
W(z)
y
x
P(z)
H’(z)
x

## Slide 26: Feedforward ANC – Filtered-x LMS
  Convergence is dependent on secondary path. Step size bounds assuming white reference signal [1]
  hence (long) H(z) implies smaller μ & slower convergence
  Stability also affected by the accuracy of secondary path estimate H’(z). Filtered-X LMS found to be robust to errors in H’(z)… (details omitted)
  Note that adaptation in “first-H’(z)-then-W(z)” (as in p.24) relies on error signal (e) from “first-W(z)-then-H(z)”, which is inconsistent…
Equivalent delay of secondary path
Length of control filter
Power of filtered
reference signal
[1] I. Tabatabaei Ardekani and W. H. Abdulla, ‘Theoretical convergence analysis of FxLMS algorithm’, Signal Processing, vol. 90, no. 12, pp. 3046–3055, Dec. 2010,

## Slide 27: Feedforward ANC – Filtered-x LMS
Improved version is ‘Modified Filtered-x LMS’
H(z)
d
e
W(z)
y
x
P(z)
H’(z)
x
H’(z)
d’ (=estimate of d)
W(z)
copy
-
+
+
+

## Slide 28: Feedforward ANC – Filtered-x LMS
Improved version is ‘Modified Filtered-x LMS’
(continued)
    Note that ( if H’(z)=H(z), hence d’=d ) adaptation in “first-H’(z)-then-W(z)” now relies on error signal (e) from “first-H’(z)-then-W(z)”, which is consistent
    Hence improved convergence (can use larger step size)
    Hence can also replace LMS by RLS (=‘Modified Filtered-x RLS’)

## Slide 29: Feedforward ANC
  Additional problem: Feedback (previously assumed to be negligible)
  Feedback from secondary source (loudspeaker) into ref. microphone
  This is an acoustic echo cancellation/feedback problem :
  Fixed AFC based on given F(z) (obtained through calibration) is easy
  Adaptive AFC is problematic (combination of 2 adaptive systems)
H(z)
d
e
W(z)
y
secondary
source
primary
source
x
F(z)
Skip this slide

## Slide 30: Feedforward ANC - MIMO
Extension:
Multiple reference signals
Multiple secondary sources
Multiple error signals
  (a.k.a. ‘MIMO ANC’, multiple-input multiple-output ANC)
  Applications: airplane/car cabin noise control, active vibration control,...
  Needs generalization of Filtered-x algorithms, where coefficients of control filters are adapted to minimize the sum of the mean square values of all the error signals.

## Slide 31: Feedforward ANC - MIMO
R reference microphones
L loudspeakers
M error microphones
One secondary path per loudspeaker-error micr. pair (L x M)
Signal at microphone m is...
One control filter per ref.micr.-loudspeaker pair (R x L)
Loudspeaker signal is sum of contributions from all reference signals r
ml

## Slide 32: Feedforward ANC - MIMO
Every reference signal is filtered by every secondary path
i.e. number of filtering operations is R x L x M (!)
If secondary paths are high-order FIR, leads to (extremely) high computational complexity
Leads to MIMO Fx-LMS
Minimize MSE (summed over error microphones)

## Slide 33: Feedback ANC
Basic set-up:
  H(z) = secondary path
  1 microphone instead of 2 microphones
  Applications : active headsets, ear defenders
    (e.g.10-15dB reduction achieved for frequencies 30-500Hz)
W(z)
H(z)
primary source
d
e
y
secondary source

## Slide 34: Feedback ANC
Design problem:
If H(z) is given design W(z) (=feedback control) such that E(z) is `minimized’
For `flat’ H(z)=Cnt : W(z)=-A for large A (as in an opamp)
For general H(z) : see control courses
W(z)
H(z)
d
e
y
+

## Slide 35: Feedback ANC
An interesting feedback controller is formed as follows :
…with H’(z) an estimate of H(z) and W(z) yet to be defined.
Note that if H’(z)=H(z), then W(z) is fed by d(n), i.e. …
d
e
+
W(z)
H(z)
y
-H’(z)
+

## Slide 36: Feedback ANC
Note that if H’(z)=H(z), then W(z) is fed by d(n), i.e. …
…which means the feedback system has been
transformed into a feedforward system,..
d
e
+
W(z)
H(z)
y
d

## Slide 37: Feedback ANC
In the set-up of p.18, this is …
  With P(z) =1, and for instance for H(z) containing pure delay, this means W(z) must act as a predictor for d
  Adaptation of W(z) based on (modified) filtered-X algorithm
H(z)
d
e
W(z)
y
secondary
path
primary
source
x
1

## Slide 38: Feedback ANC
With H’(z)≠H(z) and modified Fx-LMS algorithm, this is...
Note that the error microphone signal (to the right) is used to replace the (non-existing) input (=noise reference) microphone signal (to the left). However, this error microphone signal has a contribution from the secondary loudspeaker signal (through C(z)), which is then as if the input microphone were affected by feedback (through C(z), see p15). The subtraction of the filtered loudspeaker signal (filtered by C’z) then also acts as a feedback cancellation.
Compare to p.12 !
H(z)
H’(z)
H’(z)

## Slide 39: Feedback ANC
With H’(z)≠H(z) and modified Fx-LMS algorithm, this is...
  Note that the error microphone signal (to the right) is used to replace the (non-existing) noise reference microphone signal (to the left)
  However, this error microphone signal has a contribution from the secondary loudspeaker signal (through H(z)), which is then as if the input microphone were affected by feedback (through H(z))
  The subtraction of the filtered loudspeaker signal (filtered by H’z) then also acts as a feedback cancellation.

## Slide 40: Conclusion
www.harman.com
www.silentium.com
Sound zone control
Considered fixed control filter design
  Pressure Matching
  Acoustic Contrast Control
Active noise control
Considered adaptive control filter design
  Feedforward ANC
  Feedback ANC
PS: Can also consider sound zoning with
adaptive control filters (how?)